## Slide 1
Chapter 4
Principle of staining

## Slide 2: Content
Introduction
Types of stain
Affinity of staining
Factors that determine selectivity of stain
Types of commonly used stains in histopathologic techniques

## Slide 3: Learning objectives
Upon completion of this chapter, the student will be able to:
Define staining.
Discuss factors that contribute to dye-tissue affinity.
Explain factors affecting selectivity of stain.
Explain the classification of hematoxylin on the basis of mordant used.

## Slide 4: 5.1. Introduction
Staining:
is a biochemical technique of adding a classic specific dye to a substrate:
  DNA
  Proteins
  Lipids and
  Carbohydrates
To qualify or quantify the presence of a specific compound.
Notes: In staining of tissues and cells, we should know the properties of tissues, cells and stain. Then we can know how tissues and cells are stained and what affects them.

## Slide 5
Staining always involves the visual labeling of some biological entity by attaching, or depositing in its vicinity, a marker of characteristic color or form.
Stain is the marker, or the reagent used to generate the marker.

## Slide 6
Why do any tissue components stain?
Why do stained components remain stained?
Why are all components not stained?
Sections stained with either acid or basic dyes are usually mounted in non-aqueous media to prevent extraction of dye.

## Slide 7: 5.2. Types of stain
1. Negative stain :
is the type of stain that does not color the tissue or cells but surrounds the tissue.
uncolored tissue can be seen against a background color.
2. Supravital staining is the stain taken by living cells.
3. Special stain is the stain that identifies various specialized structures. e.g. capsule, collagen, glycogen,etc.
4. Differential stain the stain uses two or more dyes that react differently.

## Slide 8
Principle of staining:
Enhance natural contrast and to make more evident various cell and tissue components and extrinsic material.
Most of the dyes behave like acidic or basic compounds and have a tendency to form electrostatic (salt) linkages with ionizable radicals of the tissues.
Tissue components that stain more readily with basic dyes are termed basophilic & those with an affinity for acid dyes are termed acidophilic.

## Slide 9: Staining…..
The unstained slide must go through the reverse process that it went through from paraffin section dewaxing to water(rehydration) . C:\Users\user\Downloads\Video\Histopathology - tissue processing.MP4
The stained slide is taken through
  dehydration,
  clearing agents to a point at which a permanent resinous substance beneath the glass cover slip (Mounting)
  C:\Users\user\Downloads\Video\Histological staining- hematoxylin & eosin - YouTube.MP4

## Slide 10: 5.3. Affinity of staining
Affinity describes the tendency of a stain to transfer from solution onto a section.
Affinity is not a one-way procedure but a two-way procedure as it depends on the tissue as well as on the dye.
Factors affecting staining of tissues:
  Solvent-solvent interaction (Hydrophobic bonding)
  Reagent-reagent interaction
  Reagent-tissue interaction (Vander -Waal forces)
  Columbic attraction
  Hydrogen bonding
  Covalent bonding.

## Slide 11: 5.3.1. Solvent-solvent interaction
There is a tendency of hydrophobic grouping or chemicals or substances to come together even though initially dispersed in aqueous (water) solution.
The water molecules are transiently held together in clusters by hydrogen bonding.
These clusters are stabilized by hydrophobic group
Any process that involves breakup of the clusters in to disorganized water molecules will tend to occur spontaneously.
Phenylalanine and tryptophan side chains or biphenyl naphthol are hydrophobic grouping.

## Slide 12: 5.3.2. Reagent-reagent interaction
Dye interacts with each other and form aggregates.
Dye aggregation increases with concentration.
Cations or basic dyes build up in tissues where there is high negative charge such as;
  - polysaccharides in mast cell granules and
  - cartilage matrix.

## Slide 13: Reagent-reagent ……
Metachromatic staining :
This is due to dye aggregation having spectral properties unlike those of monomeric dyes.
Metachromasia takes place when certain negatively charged groups on the tissue react with cationic dyes.
On polymerization the original color of the dye changes to another color (eg mast cell stain pink with toluidine blue).
Silver impregnation technique: stain-stain
Gomer’s type enzyme histochemistry: interaction

## Slide 14: 5.3.3. Dye-tissue interaction or Vander- Walls reaction
Van-deer-Walls force:
acts between dye and tissues.
is of short range.
Van-deer-Walls force is strong where close reagent contact is possible.
The attraction of intermolecular forces between molecules
Notes: Therefore, Van-deer-Walls force is strong where close reagent contact is possible.
And use of dye and substrate that are easy to polarize result in strong interaction.

## Slide 15: Van-deer-Walls force….
Substrates and chemicals that favor Van-deer-walls bonding include:
Tyrosine and tryptophan residues of proteins;
Heterocyclic bases of nucleoproteins;
Halogenated dyes such as,
- rose Bengal,
- phloxine,
- enzyme substrate,
- naphthyl indoxyl system.

## Slide 16: 5.3.4 Columbic attraction
Is termed as salt link or electrostatic bond.
The electrostatic bonds arise from electrostatic attraction of unlike ions
is the most widely acknowledged reagent-tissue interaction.
Example:
The colored cation of basic dyes and tissue structures rich in anion such as - phosphated DNA and RNA
- carboxylated or
- sulphated mucosubstances.
Notes: Columbic attraction
Columbic attraction is the most widely acknowledged reagent tissue interaction. It is also termed as salt link or electrostatic bond. The electrostatic bonds arise from electrostatic attraction of dissimilar ions, example, the colored cation of basic dyes and tissue structures
rich in anion such as phosphated DNA and RNA and carboxylated or sulphated mucosubstances.
In case of columbic attraction, the amount of dye able to enter a given tissue will depend on charge of dye, magnitude of charges, amount of non-electrolyte present in dye bath and ability of tissue to sink or swell.

## Slide 17: Columbic attraction…..
In case of columbic attraction, the amount of dye able to enter a given tissue will depend on:
charge of dye,
magnitude of charges,
amount of non-electrolyte present in dye bath
ability of tissue to shrink or swell.

## Slide 18: 5.3.5. Hydrogen bonding
Hydrogen bonding(H-bonding)
is a localized bond when a hydrogen atom lies b/n two electronegative atoms such as ,H and N .
It will rarely be an important source of reagent-tissue affinity when aqueous solvents are used.
If dye is taken by other process, H- bonding may subsequently contribute to affinity.
Notes: In non-aqueous solution, hydrogen bonding may play a more significant role, as with Best’s carmine stain for glycogen. In this staining procedure, the solvent in major part is methanol.

## Slide 19: 5.4. Factors that determine selectivity of stain
Dye or stains are not taken by every part of tissue, and this is called selectivity of stain.
Factors that determine selectivity of stain include:
  Number and affinity of binding sites
  Rates of reagent uptake
  Rate of reaction
  Rate of reagent loss.

## Slide 20: a) Number and affinity of binding sites
The staining affinity of dye depends on:
  the number of binding sites of the dye to tissue.
Reagent-tissue affinities and the number of binding site vary.
Example
Non-ionic Sudan dye will have affinity for fat droplets, but none for the surrounding hydrated proteins.
Therefore, Sudan stains intensely fat tissues and not proteins or carbohydrates.
Notes: In a covalent bonding system, reagents are chosen so that colored reaction is formed only from limited range tissue chemical groupings. For example, in Feulgen nuclear stain, PAS gives red color only with nuclear DNA. Some dyes have high affinity for certain chemicals in tissue and no affinity for other chemicals in the tissue. For instance, in routine H & E stain, Hematoxyline has affinity for nucleus and Eosin for cytoplasm. The negatively charged acid dyes have high affinity for tissue carrying cationic charges (Proteins under acidic condition).

## Slide 21: b)Rate of reagent uptake by the tissue
Selectivity of the stain by the tissue depends on the rate of reagent uptake by the tissue.
Therefore, selectivity can be controlled by modifying the time of staining.
Example:
short period of staining :
Mucin-staining method using Alcian blue or colloidal iron.
prolonged period of staining:
Nucleic acid and RNA-rich cytoplasm are also stained using Alcian blue or colloidal iron.

## Slide 22: Rate of reagent uptake……
There are methods where three or more dyes diffuse at varying rates, as a result different structures can be stained by different dyes.
Example
Collagen fibers stain rapidly while the muscle fibers stain at intermediate rate

## Slide 23: c) Rate of reaction
Selectivity of the stain also depends on the rate of reaction. This is because,
  reactive stain yield colored derivatives, &
  amount of color depend on the selective rates of reaction.
Example:
The periodic acid oxidation step of the periodic acid-Schiff procedure, if sufficiently prolonged, oxidize various chemical structures present in tissue.
Notes: In histochemical procedure, the oxidation time is chosen to Aldehydes generation to the fast reacting 1, 2 diol grouping, plentiful in polysaccharides.

## Slide 24: Rate of reaction cont’d
Enzyme histochemistry provides many other examples of reaction rates that affect selectivity.
Example
At low pH, the hydrolysis of an organic phosphate applied to a tissue section in a suitable incubation media will be rapid in those parts of the tissue containing acid phosphates.
However, in structures containing alkaline phosphatase , the hydrolysis rate will be very slow.

## Slide 25: d) Rate of reagent loss
Some tissues or structures are stained and decolorized readily while other tissues or structures are not decolorized readily.
Differentiation is when a decolorized tissue takes up the counter stain.
Example; staining of muscle striation with iron Haematoxyline and myelin sheath with Luxol Fast Blue.
In regressive staining all structures are first stained quite non-selectively some times with the assistance of penetration aid such as heat or phenol.

## Slide 26: Rate of reagent loss….
The staining conditions chosen to maximize selective affinity:
Basic dyes must be applied from neutral or acidic solution.
The concentration of inorganic salt present in a dye bath ,called critical electrolyte concentration.
rate of reagent uptake, or subsequent reaction or loss of reagent or product.
Notes: The following staining conditions are chosen to maximize selective affinity.
Basic dyes must be applied from neutral or acidic solution because under alkaline
conditions, proteins themselves carry an overall negative charge, so will take up basic
dye;
Intensity of staining reaction can also be modified by varying the concentration of
inorganic salt present in a dye bath. This is called critical electrolyte concentration;
Selectivity of staining can also be achieved even if the dye-tissue affinities and the
number of binding site, of the two structures are the same. This is because the rate of
reagent uptake, or subsequent reaction or loss of reagent or product might not be the
same.

## Slide 27: 5.5. Types of commonly used stains in histopathologic techniques
1) Haematoxylin (H)
is the most popular & widely used histologic stain.
extracted from heartwood of the tree called Haematoxylin campechium with hot water.
can demonstrate clearly enormous number of different tissue structures.

## Slide 28: Natural oxidation of Haematoxyline
1. Natural oxidation(ripening) :
is exposing haematoxyline to light & air and converting it to hematin.
is a slow process, it may takes 3-4 months.
the hematin solution retains its staining ability for a long time.
Examples:
-Ehrlichs haematoxylin
-Delafield’s haematoxylin

## Slide 29: Haematoxyline…..
Haematoxylin also stains tissues that are processed by various methods.
In the routine H & E stain, nuclei stain blue-black with good intranuclear details.
While Eosin stains cytoplasm and connective tissue in varying intensity of pink, orange & red.
Haematoxylin by itself is not stain but haematin, an oxidant product of Haematoxylin is a stain & a natural dye.

## Slide 30: Production of haematin from Haematoxylin
Haematoxylin is extracted from heartwood or logwood.
It is precipitated by using urea.
Haematin is produced from Haematoxylin by two ways.
1. Natural oxidation or ripening of Haematoxylin.
2. Chemical oxidation of Haematoxyline; sodium iodate & Mercuric oxide.
.

## Slide 31: 2. Chemical oxidation
The use of chemical oxidizing agents converts the hematoxylin to hematein almost instantaneously,
are ready for use immediately after preparation.
They have a shorter useful life than the naturally oxidized hematoxylins, probably because the continuing oxidation process in air and light eventually destroys much of the hematein, converting it to a colorless compound.
Hematein is anionic, having a poor affinity for tissue, and is inadequate as a nuclear stain without the presence of a mordant.

## Slide 32: Chemical oxidation……
The most useful mordants are salts of aluminum, iron, and tungsten.
Advantages:
  Oxidize haematoxylin almost instantaneously;
  Ready to be used after immediate preparation.
Disadvantage:
  have shorter useful life when compared to naturally ripened haematoxylin.
Notes: Haematin by itself is a poor stain because it has poor affinity for tissues. Haematin is inadequate as nuclear staining without a mordant. The most useful mordants are salts of aluminum, iron, and tungsten. Lead mordants are occasionally used, for example, in demonstration of argyrophil cells.

## Slide 33: Classification of haematoxyline based on mordant used
Classification of haematoxyline based on mordant:
Alum haematoxylin;
Iron haematoxylin;
Tungsten haematoxylin;
Molybdenum haematoxylin;
Lead haematoxylin;
Haematoxylin with out mordant.

## Slide 34: 2) Eosin
Eosin
is a xanthene dye
is the most suitable stain when combined with Haematoxylin.
used to distinguish & differentiate the cytoplasm of d/t types of cells.
Therefore, different types of cells & connective tissue fibers can be distinguished

## Slide 35: Eosin…
Types of eosin
  Eosin Y (eosin yellow);
  Ethyl eosin;
  Eosin B (eosin bluish).
Eosin Y
  Most widely used eosin;
  It is a water-soluble stain and also satisfactorily soluble in alcohol.

## Slide 36: Eosin…
Eosin solution:
0.5 to 1 % solution is prepared in water.
A crystal of thymol is added to prevent fungal growth and the addition of little acetic acid sharpens the staining.

## Slide 37: Eosin…
Use of eosin stains:
Eosin stains can be used as differential stain.
Differentiation of eosin staining occurs with tap water.
Further differentiation occurs during dehydration through alcohols.
The intensity of eosin staining and degree of differentiation depend on the examining pathologist.

## Slide 38: Eosin…
Adequate differentiation may be difficult if tissue has been fixed in mercuric oxide.
Over differentiation of eosin may be continued until only RBC & granules of eosinophils are stained.
This method helps in location & identification of eosinophils.

## Slide 39: Eosin…
Ethyl eosin and Eosin B
Ethyl eosin and Eosin B are rarely used, for example, in Harri’s stain for Negri bodies.
Eosin substitutes
Certain red dyes are alternatively used as eosin.
They are phloxine, Biebrich scarlet etc.
But these chemicals give a more intense red color to tissues and rarely give subtle differentiation & hence, they are less valuable.

## Slide 40: Hematoxylin and eosin stain for paraffin sections Method
Dewax sections, rehydrate through descending grades of alcohol to water.
2. Remove fixation pigments if necessary.
3. Stain in an alumhematoxylin of choice for a suitable time.
4. Wash well in running tap water until sections ‘blue’ for 5 minutes or less
5. Differentiate in 1% acid alcohol (1% HCl in 70% alcohol) for 5–10 seconds.

## Slide 41: Hematoxylin and eosin stain for…
6. Wash well in tap water until sections are again ‘blue’ (10–15 minutes), or 7. Blue by dipping in an alkaline solution (e.g. ammonia water), followed by a 5-minute tap water wash. 8. Stain in 1% eosin Y for 10 minutes. 9. Wash in running tap water for 1–5 minutes. 10. Dehydrate through alcohols, clear, and mount

## Slide 42: 5.6. Quick haematoloxylin and eosin stain for urgent frozen section
Tissue is frozen onto a chuck using aerosol spray.
2. Cut sections with cryostat of thickness from 3-6 microns.
3. Dip in neutral 10% solutions at room temperature for 20 seconds to fix.
4. Rinse in tap water.
5. Dip in double strength Carazi’s haematoxylin to stain.

## Slide 43: Quick haematoloxylin and eosin….
6. Dip and rinse in tap water for 10 to 20 seconds.
7. Dip in 1% aqueous eosin for 10 seconds.
8. Dip in tap and rinse.
9. Dehydrate as usual in 50% ,70%, 90%, and 100% alcohol.
10. Clear with xylene and Mount in DPX