## Slide 1
Debre Markos University
ደብረ ማርቆስ ዩኒቨርስቲ
Debre Markos Institute of Technology
ደብረ ማርቆስ ቴክኖሎጂ ኢንስቲትዩት
School of Electrical and Computer Engineering
Sensing and Estimation
Industrial Automation and Introduction to Robotics
Tesfaye M.
Industrial Control Engineering, SECE, DMiT.
Notes: <number>

## Slide 2: Sensing and Estimation
Introduction
Sensors are used for internal feedback control and external interaction with the outside environment.
Animals and humans have similar distinct sensors.
A huge array of sensors is available for measuring almost any phenomenon.
In this chapter, we only discuss sensors used in robotics and automatic manufacturing.

## Slide 3: Sensing and Estimation
Sensor in robotics
Sensors can be categorized in variety of ways based on their characteristics, what they measure, and applications.
In robotics, sensors are used to measure internal and external status of the robot;
those which measure the internal status is called proprioceptive while sensors that measure the ambient is called Exteroceptive.
Proprioceptive sensors are used to measure the internal state of a robot, which might include position of different degrees of freedom, temperature, voltage on key components, motor current, and force applied to an effector.
Exteroceptive sensors detects the environmental conditions such as distance from object, light intensity, environmental temperature, interaction forces, tissue density, and so forth.
Exteroceptive sensor measurements are interpreted by the robot to extract useful environmental features.

## Slide 4: Sensing and estimation
Cont.….
Based on a capability of the sensors to generate electrical signal, sensors can be categorized into active and passive.
Passive sensors are measure ambient environment energy entering the sensor or output signal is almost provided by the measured signal without excitation (thermocouple)
Active sensors are emit energy into environment and then measure the environmental action or requires an external source of power to give out put signal (ultrasonic sensor)
Usually, active sensors are more robust than passive sensors since they have a little control over ambient condition or stimuli.
Exteroceptive sensors can be categorized further into contact and non-contact sensing.
The non-contact sensors can be used for estimation of physical properties from distance, such as intensity, range, temperature, direction, size, etc.

## Slide 5: Sensing and estimation
Measurement of both electrical and non-electrical quantities are required industrial systems and research.
The electrical quantities includes: voltage, current, impedance parameters, and phase, frequency and time.
The non-electrical measurand may be force, velocity, accelerations, mass, pressure, strain, etc.
Measurement of non-electrical quantities requires application of transducers, a device that converts non-electrical quantities or signals into electrical signal that can be conditioned.

## Slide 6: Sensing and estimation
Classification of Transducers
A transducer is a device that converts a signal from one physical form to a corresponding signal having a different physical form. Therefore, it is an energy converter. “
Input signals may be electrical, mechanical, thermal, magnetic, chemical, and radiation (corpuscular and electromagnetic).
Sensors are a device which can quantitatively measure a certain quantity and ideally no energy is drawn from a system being measured.

## Slide 7: Sensing and estimation
Sensors Used in Robotics Position potentiometer Resolver encoder Velocity encoder tachometer Force/torque Spring Strain gauges Touch/Tactile sensors Capacitive touch sensor | Range finders Vision Camera Stereo vision Sniff Taste Speech synthesizers Speech recognition Proximity You can design your own sensor so that the sensor can do as you wish!!!

## Slide 8: Sensing and estimation
Sensor Characteristics
Cost
Size
Weight
Type of output (digital or analog): Determines necessity of ADC and/or DAC
Interfacing
Resolution

## Slide 9: Sensing and estimation
Sensor Characteristics: Cont.
Sensitivity: The ratio of a change in output in response to
a change in input.
Linearity
Range: The smallest to the largest outputs
Response time:
  Usually expressed as 95% of total change.
  A special response time of 63.2% is called time constant.
  Rise time is the time required between 10% and 90% of the final value.
  Settling time is the time between 0% and 98% rise.

## Slide 10: Sensing and estimation
Sensor Characteristics: Cont.
Frequency response(military, underwater and aerospace)
Reliability
Accuracy
Repeatability

## Slide 11: Position Sensors :Potentiometers
Used as internal feedback sensors
Used both alone as well as together with other sensors such as encoders.
Analog output
Rotary or linear
Single- or multiple-turn
If wire-wound, output is stepwise.
If conductive polymer resistor paste, output is continuous.

## Slide 12: Position Sensors : Encoders
Digital output
Produces a signal for each small portion of a movement.
The disk or strip is divided into small sections.
Opaque versus transparent, reflective versus nonreflective.
Linear or rotary
A light source, such as an LED on one side, light-sensitive sensor, such as a phototransistor on the other.

## Slide 13: Position Sensors : Incremental Encoders
The sections are all equal and repeating.
Each represents an equal angle of rotation.
Only the change in position can be measured, not the absolute position.
Direction cannot be measured unless two sets of slots (2 bits) are used (1/2 step out of phase)
Can be very high resolution.
Simple to use; few output lines.

## Slide 14: Position Sensors : Incremental Encoders, cont.
Only leading and/or trailing edges must be measured.

## Slide 15: Position Sensors : Absolute Encoders
Each portion has a unique combination of clear/opaque sections
Absolute position can be measured.
Higher resolutions require many input lines.
Binary or Gray Code
  Gray code involves only one change at any time

## Slide 16: Gray code

## Slide 17: Position Sensors: Linear Variable Differential Transformer (LVDT)
A transformer whose core moves with the distance measured
Outputs is a variable analog voltage
Reliable, simple design, with linear output.

## Slide 18: Position Sensors: Resolvers
Resolvers are very similar to LVDTs in principle
Used to measure an angular motion.
A resolver is also a transformer;
  The primary coil is connected to the rotating shaft and carries an alternating current.
  Two secondary coils, placed 90 degrees apart from each other.
  When the primary is parallel to either of the two secondary coils, the voltage induced is maximum
  When they are perpendicular, the voltage is zero.
  Output is an analog sine/cosine function.

## Slide 19: Position Sensors: (Linear) Magnetostrictive Displacement Transducers (LMDT or MDT)
A pulse is sent through a conductor, which bounces back as it reaches a magnet.
The time of travel to the magnet and back is converted to a distance.
By attaching the moving part to either the magnet or the conductor, the displacement can be measured.

## Slide 20: Hall-effect sensors
Hall-effect Sensors: The output voltage of a conductor that carries a current changes when in the presence of a magnetic field.
A Hall-effect transducer’s output is analog and must be converted for digital applications.
Used in many applications, including the sensing of the position of the permanent magnet rotors of brushless DC motors.

## Slide 21: Global Positioning System(GPS)
Used in mobile robots and navigation systems to determine the current position of the device relative to a global reference frame.
The system includes many satellites orbiting the Earth at about 20,000 km, a control and monitoring station on Earth, and the GPS receivers.
The receiver uses the transmitted data from the satellites to calculate its position. This information can be sent directly to the control system of a mobile robot for positioning purposes and navigation.
Each satellite sends signals at precise intervals with information about the time the signal was sent and location of the satellite.
The GPS unit reads the signals sent by four satellites, and using the difference between the current time and the time at which each signal was sent calculates the distance to the satellite.
Each distance forms a sphere centered at the satellite, on which the GPS unit resides. The intersection between these spheres is the location of the GPS unit.

## Slide 22: Velocity Sensors
Encoders:
  Count number of signals in a given length of time to calculate velocity.
  If motion is slow, count is low and velocity is inaccurate.
  If the time is increased, velocity is not updated fast enough.
  dt may be varied depending on the angular velocity
Tachometers:
  Analog output.

## Slide 23: Velocity Sensors: Cont.
Differentiation of Position Signal:
  Signal must be as continuous as possible
  Use potentiometers with conductive polymer film

## Slide 24: Force Sensors
Piezoelectric:
  Analog output voltage
  Must be conditioned and amplified for use.
Force Sensing Resistor:
  A polymer thick-film device
  Some use a piezo paste
  Resistance decreases as force increases

## Slide 25: Force Sensors: Cont.
Strain Gauges:
  Adjust R4 in the Wheatstone bridge until current in galvanometer is zero.

## Slide 26: Torque Sensors
Measured by a pair of strategically placed force sensors.
Pairs in different planes measure force and torque in those planes.
Courtesy of ATI Industrial Automation

## Slide 27: Touch and Tactile Sensors
Touch sensors send a signal when physical contact has been made.
A tactile sensor is an array of touch sensors.
It can provide additional information about the object such as shape, size, or type of material.
Different sensors can be used for this purpose.

## Slide 28: Proximity Sensors
Used to determine that an object is close to another object before contact is made.
Magnetic:
  Activated when they are close to a magnet.
Optical:
  Receiver can only see the signal when within a range.

## Slide 29: Proximity Sensors: Cont.
Ultrasonic:
  The emitter emits frequent bursts of high frequency sound waves.
  Opposed mode and echo (diffused) mode.
  Cannot be used with surfaces that do not reflect the sound waves.

## Slide 30: Proximity Sensors: Cont.
Inductive:
  Used to detect metal surfaces.
  A coil with a ferrite core, an oscillator/detector, and a solid state switch.
Capacitive:
  Reacts to the presence of objects with a dielectric constant more than 1.2.
  Can detect non-metal materials such as wood, liquids, and chemicals.
Eddy Current:
  Based on back-emf principle
  Has two coils, one generates a changing magnetic flux as reference.
  In close proximity of conducting materials, a magnetic flux opposite of the first coil’s is generated.
  The change is proportional to proximity of the conducting material, and is measured by the second coil.

## Slide 31: Range-finders
Used to find larger distances, to detect obstacles, and to map the surfaces of objects.
Meant to provide advance information to the system.
Generally based on light--visible light, infrared light, or laser-- and ultrasonics.
Two common methods of measurement are triangulation and time-of-flight or lapsed time.

## Slide 32: Range-finders: Triangulation
The range or depth is calculated from the triangle formed between the receiver, the light source, and the spot on the object.
This only occurs at one particular instant.
The emitter is rotated (through a rotating mirror) until the spot is seen.
The angle is recorded.

## Slide 33: Range-finders: Time of Flight or Lapsed Time
Ranging consists of sending a signal from a transmitter that bounces back from an object and is received by a receiver.
The distance between the object and the sensor is half the distance traveled by the signal.
Range is calculated by measuring the time of flight and knowing its speed of travel.

## Slide 34: Range Finders: Ultrasonics
Rugged, simple, inexpensive, and low powered.
Readily used in cameras, for motion detection and navigation.
Limited resolution due to wavelength of the sound and variations of temperature and velocity in the medium.
Maximum range is limited by the absorption of ultrasound energy in the medium.
Typical frequency range of 20 kHz to above 2 MHz.
Most measure the distance using the time-of-flight technique.
Higher frequencies yield a better resolution, but attenuate much faster.
Lower frequency transducers have wide beam angles, therefore inaccurate.

## Slide 35: Range Finders: Light-Based
Based on the following methods:
  Direct time delay measurement,
  Indirect amplitude modulation,
  Triangulation.
  Stereo imaging
  LiDAR (Light Detection and Ranging), similar to radar
  Courtesy of Velodyne

## Slide 36: Voice Recognition
Involves determining what is said and taking an action based on the perceived information.
Generally works on the frequency content of spoken words.
Every word is decomposed into its constituent frequencies with a unique signature. Allow the system to recognize the word.
The user must train the system by speaking the words a priori.
Creates a look-up table of the major frequencies.
Tries to match with the information in the look-up table.
Recognition affected by variations in volume, accent, speed, etc.
More accurate look-up table makes recognition more difficult.

## Slide 37: Voice Synthesis
Voice synthesis is accomplished in two different ways.
Recreating words by combining phonemes and vowels.
  Unlimited,
  Unnatural sound,
  Phoneme chips can be used.
Recorded information.
  Limited,
  Sounds natural
  Used when all words are known a-priori.

## Slide 38: Remote Center Compliance (RCC) Device
. Not a sensor, but is used to add selective compliance to a robot.
An attachment added between the wrist and the end effector.
Meant to overcome misalignments

## Slide 39: Remote Center Compliance (RCC) Device: Cont.
It is principally a 4-bar mechanism.
The instantaneous center of zero velocity for the coupler link is at point IC.

## Slide 40: Remote Center Compliance (RCC) Device: Cont.
If linkages are equal in length in a rectangular format, coupler moves in translation.
It provides lateral flexibility only.
If linkages are in a trapezoid format, coupler rotates about the center.
It provides lateral rotation.

## Slide 41: Remote Center Compliance (RCC) Device: Cont.
RCC device is principally a combination of both.
Courtesy of ATI Industrial Automation

## Slide 42
Thank you!!!